## Slide 1: LDD Exam
EnsiCaen – SATE 3A
2019/2020
Read the attached Linux device driver.
The source has been simplified to reduce printing for this exam.
Write and draw the SART view of this driver as explained next slide.

## Slide 2: SART - Data flow and real time example
External entity
Function
Control
Data
Storage
Mouse
ISR
Sampling
dx,dy,buttons
Provide data flow and real time diagram of the driver. Use:
  Box for external entity like HW
  Bubble for function
  Stack for data storage
  Plain arrow for data flow
  Dashed arrow for control flow

## Slide 3: I3C Device Driver Data Structure Breakdown
For your convenience, here is the data structure breakdown of the I3C device driver. This may help you to better understand the source code.

## Slide 4: I3C Protocol
MIPI standardized protocol designed to overcome I2C limitations (limited speed, external signals needed for interrupts, no automatic detection of the devices connected to the bus, …) while remaining power-efficient
Extra Documentation

## Slide 5: I3C Transfer Type
I3C defines 3 different classes of transfer in addition to I2C transfers which are here for backward compatibility with I2C devices.
I3C CCC commands
  CCC (Common Command Code) commands are meant to be used for anything that is related to bus management and all features that are common to a set of devices.
I3C Private SDR transfers
  Private SDR (Single Data Rate) transfers should be used for anything that is device specific and does not require high transfer speed.
I3C HDR commands
  HDR commands should be used for anything that is device specific and requires high transfer speed.
Extra Documentation