## Slide 1: Linux Driver Analysis
EnsiCaen – SATE 3A
2015/2016

## Slide 2: Linux Kernel Driver Analysis
Get PN547 NFC driver from kernel source: pn5xx_i2c.c /!\ This code has been simplified to fit 4 paper pages
Provide data flow and real time diagram of the driver (6 points). Use:
  Box for external entity like HW
  Bubble for function
  Stack for data storage
  Plain arrow for data flow
  Dashed arrow for control flow
Provide a fix to the bug depicted slide 6 (4 points)

## Slide 3: Data flow and real time example
External entity
Function
Control
Data
Storage
Mouse
ISR
Sampling
dx,dy,buttons

## Slide 4: pn5xx_i2c driver overview
The pn5xx_i2c chip is a NFC HW controller
It is controlled by the smartphone via a I2C bus
The smartphone is the master and the pn5xx_i2x chip the slave
  1) The smartphone sends a command to the pn5xx_i2c chip
    The smartphone writes the command in a i2c message
  2) pn5xx_i2c chip answers the smartphone
    2.1) The pn5xx_i2c chip set a GPIO named pn5xx_dev->irq_gpio to 1
    2.2) When the smartphone detects this GPIO is raised, it gets the pn5xx_i2c response by reading an i2c message
    2.3) After i2c message is read, the pn5xx_i2c chip set the GPIO to 0

## Slide 5: Bug solving
Description:
  I2C read is blocked randlomly
  Using printk for debug, one can see the wait_event_interruptible is never released
Analysis:
  Depict the deadlock with a message sequence chart/diagram
  Propose a fix