## Slide 1: LDD Exam
EnsiCaen – SATE 3A
2016/2017
0) Read PN547 NFC driver from kernel source: pn5xx_i2c.c /!\ This code has been simplified to fit 4 paper pages
1) Driver spec (5 points)
2) Bug fix (2 points)
3) Quizz (3 points, 4 answers per point)

## Slide 2: 0) pn5xx_i2c driver overview
The pn5xx_i2c chip is a NFC HW controller
It is controlled by the smartphone via a I2C bus
The smartphone is the master and the pn5xx_i2x chip the slave
  1) The smartphone sends a command to the pn5xx_i2c chip
    The smartphone writes the command in a i2c message
  2) pn5xx_i2c chip answers the smartphone
    2.1) The pn5xx_i2c chip set a GPIO named pn5xx_dev->irq_gpio to 1
    2.2) When the smartphone detects this GPIO is raised, it gets the pn5xx_i2c response by reading an i2c message
    2.3) After i2c message is read, the pn5xx_i2c chip set the GPIO to 0

## Slide 3: 1) Data flow and real time example
External entity
Function
Control
Data
Storage
Mouse
ISR
Sampling
dx,dy,buttons
Provide data flow and real time diagram of the driver (5 points). Use:
  Box for external entity like HW
  Bubble for function
  Stack for data storage
  Plain arrow for data flow
  Dashed arrow for control flow

## Slide 4: 2) Bug solving
Description:
  I2C read is blocked randlomly
  Using printk for debug, one can see the wait_event_interruptible is never released
Analysis:
  Depict the deadlock with a message sequence chart/diagram
  Propose a fix

## Slide 5
1-2) Open Source Software is computer software whose ________ code is
available under a _______ (or arrangement such as the public domain)
that permits users to use, change, and improve the software, and to
redistribute it in modified or unmodified form.
3) Are we software vendors ? Most software is not _____.
It is developed directly for its customer, by the customer's own employees
or by consultants who bill for the service of software creation
4-5-6) Open Source software is an enabling technology
–________ of Linux to any HW system (embedded)
–Platforms are _________ and provide the same view of data and services
–Value is no more in HW but in content and service ________ (WEB2.0)
7) How to compile a module
[ ]: make -C ~/lib/module/kernel-xxx/build M=`pwd` kernel
[ ]: gmake -C ~/lib/module/kernel-xxx/build M=`pwd` modules
[ ]: gcc -C ~/lib/module/kernel-xxx/build M=`pwd` kernel
[ ]: make -C ~/lib/module/kernel-xxx/build M=`pwd` modules
8) How to install a module:
[ ]: instmod mymodule.o
[ ]: insmodule mymodule.ko
[ ]: insmod mymodule.ko
[ ]: instalmod mymodule.o
9) Character device is accessible to userspace application by creating a device node:
[ ]: mknod /dev/demo c major_num minor_num
[ ]: mkernalnod /dev/demo c major_num
[ ]: makenod /dev/demo c major_num minor_num
[ ]: mknod /dev/demo c minor_num
10) Linux kernel semaphore: which statment is WRONG
[ ]: down -> create unkillable processes
[ ]: down_interruptible -> allow the user-space process to be interrupted by the user
[ ]: down_trylock -> returns immediately with a nonzero return value when not available
[ ]: up -> create a unkillable mutex from the user-space process
11) Which items are executed out of ATOMIC context ?
[ ]: spinlock, atomic variables, wait_event_interruptible, tasklet
[ ]: spinlock, wait_event_interruptible, jiffies, work_queue
[ ]: atomic variables, jiffies, tasklet, work_queue
[ ]: spinlock, tasklet, wait_event_interruptible, jiffies, work_queue
12) What is the Linux memory model ?
[ ]: 1 virtual in kernel, 1 virtual in user-space and 1 physical in user-space
[ ]: 1 virtual in user-space and 1 physical in kernel
[ ]: 1 virtual in kernel, 1 physical in user-space and 1 physical in kernel
[ ]: 1 virtual in kernel, 1 virtual in user-space and 1 physical in kernel
3) Quizz