## Slide 1: LDD Exam
EnsiCaen – SATE 3A
2017/2018
Read the excellent driver extracted from https://git.kernel.org, written by Clément Perrochaud (student at EnsiCaen in 2013/14) and maintained by Linus Torvalds
1) Driver spec (7 points)
2) Quizz (3 points, 4 answers per point)

## Slide 2
4 C files have been extracted and compressed into a small document. Read it, analyse data and control flow from it. Then draw the device architecture using SART method (see next slide)
/!\ This code has been simplified to fit 4 paper pages
NFC is Near Field Communication.
NCI is NFC controller Interface, a API used into smarthpone to drive the NFC chip

## Slide 3: SART - Data flow and real time example
External entity
Function
Control
Data
Storage
Mouse
ISR
Sampling
dx,dy,buttons
Provide data flow and real time diagram of the driver. Use:
  Box for external entity like HW
  Bubble for function
  Stack for data storage
  Plain arrow for data flow
  Dashed arrow for control flow

## Slide 4
1-2) Open Source Software is computer software whose ________ code is
available under a _______ (or arrangement such as the public domain)
that permits users to use, change, and improve the software, and to
redistribute it in modified or unmodified form.
3) Are we software vendors ? Most software is not _____.
It is developed directly for its customer, by the customer's own employees
or by consultants who bill for the service of software creation
4-5-6) Open Source software is an enabling technology
–________ of Linux to any HW system (embedded)
–Platforms are _________ and provide the same view of data and services
–Value is no more in HW but in content and service ________ (WEB2.0)
7) How to compile a module
[ ]: make -C ~/lib/module/kernel-xxx/build M=`pwd` kernel
[ ]: gmake -C ~/lib/module/kernel-xxx/build M=`pwd` modules
[ ]: gcc -C ~/lib/module/kernel-xxx/build M=`pwd` kernel
[ ]: make -C ~/lib/module/kernel-xxx/build M=`pwd` modules
8) How to install a module:
[ ]: instmod mymodule.o
[ ]: insmodule mymodule.ko
[ ]: insmod mymodule.ko
[ ]: instalmod mymodule.o
9) Character device is accessible to userspace application by creating a device node:
[ ]: mknod /dev/demo c major_num minor_num
[ ]: mkernalnod /dev/demo c major_num
[ ]: makenod /dev/demo c major_num minor_num
[ ]: mknod /dev/demo c minor_num
10) Linux kernel semaphore: which statment is WRONG
[ ]: down -> create unkillable processes
[ ]: down_interruptible -> allow the user-space process to be interrupted by the user
[ ]: down_trylock -> returns immediately with a nonzero return value when not available
[ ]: up -> create a unkillable mutex from the user-space process
11) Which items are executed out of ATOMIC context ?
[ ]: spinlock, atomic variables, wait_event_interruptible, tasklet
[ ]: spinlock, wait_event_interruptible, jiffies, work_queue
[ ]: atomic variables, jiffies, tasklet, work_queue
[ ]: spinlock, tasklet, wait_event_interruptible, jiffies, work_queue
12) What is the Linux memory model ?
[ ]: 1 virtual in kernel, 1 virtual in user-space and 1 physical in user-space
[ ]: 1 virtual in user-space and 1 physical in kernel
[ ]: 1 virtual in kernel, 1 physical in user-space and 1 physical in kernel
[ ]: 1 virtual in kernel, 1 virtual in user-space and 1 physical in kernel
2) Quizz

## Slide 5
open
close
send
fw dwnl
probe
remove
fw work complete
fw send chunk
fw send
fw work
fw recv frame
nxp_nci_info
init
HW
COLD
- phy_id
- nci_dev - parent device - ops:NFC PROTOCOL
KERNEL
nci_dev
NCI
COLD
write(skb)
-ESCHUTDOWN
COLD
‘free all’
COLD
fw dwnl done
nxp_nci_fw_info
FW_HDR_LEN
FW_CMD_RESET
cmd_completion
NCI_MODE_FW
read(skb)
request_fw
result
write(skb)
FW_RESET_CMD
skb